## Slide 1
Refrigeration excellence since 1962
Zanotti Industrial Division

## Slide 2
Zanotti SpA designs and manufactures refrigeration systems for the whole cold chain (commercial, industrial and transported) since 1962. Zanotti was acquired by Daikin in 2016.
Zanotti Industrial Division is located in Bologna, and it is specialized in the design and manufacturing of bespoke Ammonia and HFC/HFO refrigeration systems.
Zanotti has an extensive experience in large plants and High-Capacity Units through numerous applications in different sectors (refrigerated warehouses, clean rooms, process cooling, chemical & pharma industry, automotive and climate test chambers, ice rinks, etc).
Introduction
Tewis Smart Systems
Hubbard UK
Zanotti Pegognaga
Zanotti Transblock Italia
Zanotti Industrial Division Bologna
Via Ferrara 1, San Pietro in Casale

## Slide 3
Industrial Refrigeration Solutions
KEY POINTS
Each Unit is designed and manufactured starting from the specifications of the customers.
Design is fully customisable to match with all the Customer requirements→ i.e. reduced footprints, corrosive environments, harsh ambient temperatures, noise reduction cabinet, capacity regulation 0-100%, Power&Control Panel and VFD installed on-board or remote, etc.
Wide operational range of temperatures → Evaporating temperatures down to -50°C (Ammonia) and -40°C (R454c)
Large cooling capacities → starting from ~100 kW (typical for LT applications) up to >2 MW/each unit.
On-site Activities: Commissioning performed by Zanotti Specialists.
Ammonia Chiller and Compression Units
Low-GWP HFC/HFO Chillers
R1234ze
R1234ze
R449a
R454c
NH3
NH3
NH3

## Slide 4
Chiller Unit
NH3
Chiller Unit With Remote Condenser
Compression Units
NH3
NH3
Ammonia Solutions
 |  | Cooling Capacity per Single Unit (kW) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 50 | 100 | 150 | 175 | 200 | 250 | 300 | 400 | 500 | 600 | 800 | 1000 | 1250 | 1500 | 1600 | 1900 | 2000 | 2200 | 2500 | 2600 | 3200 | 3800 | >4000
Evaporation Temperature (°C) | -50 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -45 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -40 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -35 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | +5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | +10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Special Design (Booster)
Single Compressor Configuration
Double Compressor Configuration
Range of Regulations
MAIN FEATURES
Typical Chiller Configuration.
Compressors: Screw type (Daikin/J&E Hall) with Economiser. Oil Separator: Horizontal (Vertical for lower capacities only) Condenser: Plate HX Stainless Steel. Evaporator: Flooded Plate HX Stainless Steel. Oil Cooling Method: External water cooled, Thermosyphon, Liquid injection. Ammonia Separator: Horizontal with level control and automatic oil recovery system. Safety Valves: Double with switching valve Power&Control Panel and VFD: installed on-board or provided loose. PLC: Siemens. Installation: Indoor or Outdoor (with protective enclosure)
Chiller units are fully assembled and wired in the workshop.
Working conditions: Multiple set-points selectable (According to the compressor/unit limits).

## Slide 5
 |  | Cooling Capacity per Single Unit (kW) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 |  | 0 | 15 | 50 | 100 | 150 | 200 | 250 | 275 | 300 | 375 | 450 | 500 | 550 | 600 | 700 | 750 | 900 | 1000 | 1100 | 1250 | 1400 | 1700 | 2000 | 3000
Evaporation Temperature (°C) | -45 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -40 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -35 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -30 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -25 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -20 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -15 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | -5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | +5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | +10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Freon Solutions
Range of Regulations
R1234ze
Single Compressor
Configuration
R1234ze
Double Compressor
Configuration
R454c
Single Compressor
Configuration
R454c
Double Compressor
Configuration
Chiller Unit
Chiller Unit With Remote Condenser
Chiller Unit With Remote Evaporator
Condensing Temperature Limited to +40°C
MAIN FEATURES
Typical Chiller Configuration.
Compressors: Semi-hermetic (R454c) or Compact (R1234ze) Screw type (Bitzer) with Economiser. Oil Separator: for semi-hermetic type, Vertical Condenser: S&T or Plate HX Stainless Steel. Evaporator: S&T or DX Plate HX Stainless Steel. Oil Cooling Method: External water cooled, Thermosyphon, Liquid injection. Safety Valves: Double with switching valve Power&Control Panel and VFD: installed on-board or provided loose. PLC/controllers: Siemens, Carel, Danfoss. Installation: Indoor or Outdoor (with protective enclosure)
Chiller units are fully assembled and wired in the workshop.
Possibility to equip the units with more than 2 compressors
Low GWP refrigerant: R454c, R1234ze. Other refrigerants: R449a, R134a
R449a
R449a
R454c

## Slide 6
Case Study – Ammonia Chiller For a Climatic Test Chamber
KEY POINTS
Application: Automotive
Location: Czech Republic
Daikin Entity: DACE CZ
Variable cooling conditions, selectable by HMI: a) 2.110 kW @-4/+36°C b) 800 kW @-17/+36 °C c) 500kW @-19/+36 °C
Compact Layout: limited space available to get in the building and to reach the machine room
Regulation with VFD. (Power panel and VFD provided loose)
Idle rotation: full regulation 0-100% possible without shutting-off the compressor to eliminate start/stop waiting time. The idle rotation is based on hot gas recirculation which is activated under 25% of nominal capacity.
Chiller Unit
NH3
Delivered 2023

## Slide 7
KEY POINTS
Application: Chemical Plant, Process Cooling
Location: Italy
Daikin Entity: None, Direct Selling
Working Condition: 1.000 kW @-4/+35°C
Regulation with VFD (power panel and VFD provided loose)
Outdoor Installation: LT pipes and components coated with aluminium foils
Evaporative condenser included in the scope of supply
Case Study – Ammonia Chiller for a Chemical Plant
Chiller Unit With Remote Condenser
NH3
Delivered 2023

## Slide 8
KEY POINTS
Application: Refrigerated Warehouse
Location: Qatar
Working Conditions: 1.560 kW @+3/+40°C
Regulation with VFD (power panel and VFD installed on-board)
Indoor installation
Case Study – Ammonia Chiller For a Refrigerated Warehouse
Chiller Unit With Remote Condenser
NH3
Delivered 2023

## Slide 9
KEY POINTS
Application: Pharma Plant
Location: Austria
Working Conditions: 400 kW @-24/+44°C
Regulation with VFD (power panel and VFD installed on-board)
Outdoor installation
Double-compressor configuration
Oil cooling method: Air-cooled integrated on-board
Case Study – R454c Chiller For a Pharma Plant
Chiller Unit With Remote Evaporator
R454C
Delivered 2023

## Slide 10
KEY POINTS
Application: Refrigerated warehouse
Location: Italy
Working Conditions: 350 kW @ -12/+55°C
Power panel installed on-board
Outdoor installation
Double-compressor configuration: two independent circuits
Pumping module installed on-board
Case Study – R1234ze Chiller For a Refrigerated Warehouse
Chiller Unit With Remote Condenser
R1234ze
Delivered 2023

## Slide 11
KEY POINTS
Application: Ice Rink
Location: Hungary
Daikin Entity: DACE Hungary
Working Condition: 330 kW @-20/+43°C
Power panel installed on-board
Multi compressor configuration, with power panel on-board
Case Study – R449a Chiller For Ice Rink
Chiller Unit
NR449a
Delivered 2023

## Slide 12
Conclusions
CONTACTS
Giuseppe Masci Sales Representative E-mail: g-masci@zanotti.com Phone: +39/3442814906
Antonio Paiano Sales and Business Development Manager E-mail: a-paiano@zanotti.com Phone: +39/3442814907
PRODUCTS MAIN FEATURES
Each Unit is designed and manufactured based on customer specifications → No price list available.
Manufacturing of units operating with Ammonia or Freon (R454c, R1234ze, R449a, R134a, etc.)
High Design Flexibility → Units are fully customisable to match with all the requirements
Wide operational range of temperatures → Evaporating temperatures down to -50°C (Ammonia) and -40°C (R454c)
Large cooling capacities → starting from ~100 kW (typical for LT applications) up to >2 MW/each unit.
On-site Activities → Commissioning performed by Zanotti Specialists
TYPICAL APPLICATIONS
Refrigerated Warehouses
Process Cooling (Chemical and Pharmaceutical Plants)
Pharmaceutical
Food Processing
Ice Rinks
Test Chambers
Air Conditioning (Large Capacities Only)
WHAT WE CAN OFFER
Consulting and Design Support
Pre-assembled Units
On-site personnel for installation supervision and commissioning (either Refrigeration and Software Specialists)
Planned maintenance activities